## Slide 1: Welcome Home! Internet Open Telemetry Martin Hron security researcher

## Slide 2: Welcome to the age of speed and security!
“A computer lets you make more mistakes faster than any invention in human history - with the possible exceptions of handguns and tequila.”
Mitch Ratliff

## Slide 3
So let’s talk about the IoT

## Slide 4: Personal story
Following part of the presentation contains best practices violation, domestic violence on devices, broken security and self-confidence.

## Slide 5: Personal story: How has it started
I bought a house
I dreamt of home automation
I was confident enough that I’m able to achieve it in a DYI way.

## Slide 6: Personal story : options
use one vendor and one solution, one cloud
You’ve got a bunch of devices from different vendors or even dumb devices

## Slide 8: Personal story
Some devices might be exotic.

## Slide 10: Personal story
I had mixture of devices and a was dreaming of nice rig for my “smart hub” and all the equipment. Dreaming about a house where everything just happens.

## Slide 13: Babylon of “standards”
Physical layer / data link
  Bluetooth
  RS232, RS485, CAN, eBUS
  WiFi, Ethernet
  ZigBee
  433, 866 MHz
  and many others

## Slide 14: Babylon of “standards”
Transport / application layer
  Textual data
  JSON
  HTTP
  XML
  Binary oriented protocols
  Proprietary protocols

## Slide 16: Message Queue Telemetry Transport - MQTT
publisher - subscriber model
payload agnostic
topics can be organized in a tree like structure
when subscribing, wildcards can be used
usually operates through TCP on port 1883
supports the “last will” and persistent topics

## Slide 17: MQTT topics
Examples of the topics: /house/attic/light /house/basement/door /house/basement/light
Tree like organized structure. When subscribing, you can use wildcards. # for the all levels from here down the tree or + for any single level.
Subscription to /house/+/light delivers all light topics in any room
Subscription to only # delivers every topic published by anyone to this MQTT server

## Slide 18: Typical implementation
Mixture of devices
One namespace
MQTT broker
Business logic
Usually, this also provides some dashboard and a frontend (Domoticz, openHAB, Home Assistant, MQTT dash, Node-Red and many others)

## Slide 19: MQTT Broker typical setup of “smart home”
MQTT Broker
sensor
(switch)
sensor
(door contact)
sensor
(thermometer)
“smart breaker“ box with MQTT support
actor
(smart bulb)
actor
(garage doors)
actor/sensor
(heating unit)
bridge
sensor
(switch)
actor
(dumb bulb)
bridge
bridge
simple wire
ZigBee
ETH / WiFi
eBUS
bussines logic

## Slide 20
And what about security?
Yes! There is a security!

## Slide 21: Welcome home!

## Slide 22: Welcome home!

## Slide 23: Welcome home!
Many dashboards have no password set
There are ~49K MQTT servers available to connect
There are ~32K MQTT servers opened without any password set
Remember? You can subscribe to #

## Slide 24
Rules of the house
no real exploits
use what is available
cause no harm
even if you are tempted to do so ;)

## Slide 26
DEMO TIME

## Slide 27
Domoticz
Home Assistant

## Slide 28: Home automation software “smart hubs”
Similar concept
Provide business logic
Provide frontend / dashboard
Usually integrate with MQTT and cloud services

## Slide 29: Domoticz

## Slide 30
DEMO TIME

## Slide 31
Home Assistant: case study

## Slide 32
Home Assistant: at the same IP

## Slide 33
Home Assistant: at the same IP

## Slide 34
Home Assistant: give me your secrets

## Slide 35
Home Assistant: Welcome Home!

## Slide 36
Home Assistant: I’m not the only one

## Slide 37
Home Assistant: I’ve been hacked

## Slide 38
Home Assistant: I’ve been hacked

## Slide 39
Home Assistant: I’ve been hacked

## Slide 40
Home Assistant: I’ve been hacked

## Slide 41
Home Assistant: I’ve been hacked

## Slide 42
MQTT DASh

## Slide 43: MQTT Dash
Simple Android/IOS app
MQTT centric, simple UI that directly reflects state or controls devices through MQTT topics
Interesting concept of storing/loading whole configuration by publishing it to the “persistent” topic

## Slide 47
OWNTRACKS
PWNTRACKS

## Slide 48: Your “personal” GPS tracker
Basically Android and IOS application for GPS tracking
Supports MQTT
Forget about unsecured cameras, this is even worse.

## Slide 49
DEMO TIME

## Slide 50: Conclusion
Real world examples how bad the situation is
Educate people more about security
Educate vendors and developers
Let’s stick to the security as an opt-out choice.
DON’T STORE PASSWORDS IN PLAINTEXT
NEVER
EVER

## Slide 51: THERE IS ONLY ONE SECURITY
STOP SAYING IoT SECURITY!

## Slide 52: MQTT can be also used for automation of your garden
But the risks could be “high”

## Slide 53: Thank You! Martin Hron
@thinkcz
hron@avast.com
www.avast.com